## Slide 1
ETC2.0 — Technical Understanding
車載器 (Shasaiki) • RSU • DSRC • Application Layer
• Goal: understand what communicates with what, at which layer, and where the ETC card fits.
• Primary standards: ARIB STD-T75, STD-T88, STD-T110.
01 | ETC2.0 Technical Session

## Slide 2
What is ETC2.0?
From toll collection to vehicle–road communication
• ETC2.0 uses bidirectional communication between roadside units (RSUs) and vehicle onboard units (OBUs).
• It supports toll-related services plus traffic, route, safety and probe-data services.
• NILIM describes travel history and behavior history stored in ETC2.0 OBUs and collected as probe data at RSUs.
02 | ETC2.0 Technical Session

## Slide 3
Big-picture architecture
Keep these communication paths separate
• ETC card ↔ OBU: card-side interface inside the vehicle equipment.
• OBU ↔ RSU: ETC2.0 / DSRC wireless communication.
• RSU ↔ roadside backend: infrastructure/application processing.
• Key point: the RSU does not directly talk to the ETC card.
03 | ETC2.0 Technical Session

## Slide 4
What is 車載器 (Shasaiki)?
Vehicle-mounted equipment / OBU
• It is the vehicle-side ETC/DSRC equipment, not merely a reader.
• The ETC2.0 vehicle equipment has ETC functionality and a DSRC section for services.
• The official ETC portal states that DSRC uses ARIB STD-T75 and references JEITA TT-6002A for the vehicle-equipment DSRC section.
04 | ETC2.0 Technical Session

## Slide 5
What is DSRC?
Dedicated Short-Range Communication
• DSRC provides short-range wireless communication between roadside/base station and vehicle/mobile station.
• ARIB STD-T75 specifies the radio air interface.
• The standard defines the roadside unit as the Base Station and onboard equipment as the Land Mobile Station / Mobile Station.
05 | ETC2.0 Technical Session

## Slide 6
The standards map
Which document defines what?
• ARIB STD-T75 → DSRC radio communication interface.
• ARIB STD-T88 → DSRC Application Sub-Layer; supports multiple applications over STD-T75.
• ARIB STD-T110 → DSRC Basic Application Interface; supports non-IP applications and includes IC-card access.
• JEITA TT-6002A → ITS vehicle-mounted equipment DSRC section standard specification.
06 | ETC2.0 Technical Session

## Slide 7
Protocol-stack mental model
Do not mix radio, DSRC-ASL and application
Application / Service
DSRC Application Sub-Layer — STD-T88
DSRC System / Radio Interface — STD-T75
5.8 GHz radio path
07 | ETC2.0 Technical Session

## Slide 8
What STD-T110 adds
Application interfaces above the DSRC protocol
• OBE instruction response
• OBE memory access
• IC card access
• Push-type information delivery
• OBE ID communication
• OBE basic indication
08 | ETC2.0 Technical Session

## Slide 9
Where does the ETC card fit?
Card communication is inside the OBU context
• ETC card is inserted into the vehicle equipment.
• The OBU handles the vehicle-side card/application interaction.
• ETC2.0 DSRC communication is separately between OBU and RSU.
• Do not map WUPA/ATQA/anticollision/SELECT/RATS directly onto DSRC messages.
09 | ETC2.0 Technical Session

## Slide 10
Simplified communication sequence
Learning model — verify exact project traces/spec
• 1. Vehicle enters the RSU communication area.
• 2. RSU and OBU establish/perform DSRC communication.
• 3. Application/service is identified or invoked.
• 4. Data is exchanged for the required service.
• 5. OBU may provide stored probe information when applicable.
• 6. Communication ends as the vehicle leaves the communication area.
10 | ETC2.0 Technical Session

## Slide 11
ETC2.0 probe data
Why ETC2.0 is more than tolling
• OBU can accumulate travel history and behavior history.
• When the vehicle passes an RSU, stored information can be collected as probe data with user consent.
• Travel history helps analyze speeds/congestion.
• Behavior history helps identify frequent sudden-braking / near-miss locations.
• NILIM reports approximate OBU memory capacity of 80 km travel history and 31 behavior-history events, with older data overwritten.
11 | ETC2.0 Technical Session

## Slide 12
Communication failure — engineering view
Why RF/environment matters
• Official ETC2.0 rules warn that DSRC communication is not guaranteed under every environment.
• Factors include nearby metal/reflection, multiple onboard units, shielding/reflection from nearby vehicles, antenna obstruction and heat-reflective glass.
• Failures can therefore be RF/environmental as well as protocol/application failures.
12 | ETC2.0 Technical Session

## Slide 13
Testing perspective
From specification → conformance → logs
• ARIB TR-T16 defines compatibility-confirmation testing for DSRC mobile stations against the STD-T75 radio interface.
• A practical debug split is: RF/link → DSRC protocol → application → OBU/card → backend.
• Identify the layer before changing application logic.
13 | ETC2.0 Technical Session

## Slide 14
How this connects to our card work
Use existing knowledge carefully
• Card-side work: APDU / ISO 7816 / card state / crypto / timing.
• ETC2.0 vehicle-roadside work: DSRC / OBU / RSU / application interfaces.
• STD-T110 explicitly includes IC-card access, so the two worlds can meet inside the OBU.
• The DSRC link itself is not the same as contactless card anti-collision or APDU exchange.
14 | ETC2.0 Technical Session

## Slide 15
Key takeaways
What I should remember
• ETC2.0 = bidirectional vehicle–road infrastructure communication.
• Shasaiki = vehicle-mounted equipment / OBU.
• RSU = roadside/base station communicating with the OBU.
• STD-T75 = DSRC radio interface.
• STD-T88 = DSRC Application Sub-Layer.
• STD-T110 = basic application interfaces, including IC-card access.
• Next: study the exact project communication trace and message sequence.
15 | ETC2.0 Technical Session

## Slide 16
Official references
Use these before secondary websites
• MLIT / NILIM — ETC2.0 Probe Information
• ARIB STD-T75 — Dedicated Short-Range Communication System, Version 1.6
• ARIB STD-T88 — DSRC Application Sub-Layer, Version 1.1
• ARIB STD-T110 — DSRC Basic Application Interface, Version 1.1
• ETC General Information Portal — ETC2.0 vehicle-equipment DSRC rules
• ARIB TR-T16 — DSRC mobile-station compatibility confirmation tests
16 | ETC2.0 Technical Session